## Slide 1
WaferLLM Gap Analysis
What's needed to run full Llama3-8B inference on WSE-3
Prefill (WaferServe) | Decode (WSE-3-GQA)
April 2026

## Slide 2
Current Implementation: Single Transformer Layer
Operations supported in Prefill/WSE-3 and Decode/WSE-3-GQA
Operation | Prefill | Decode (GQA) | Notes
RMSNorm (pre-attention) | Yes | Yes | 
Q / K / V Projections | Yes | Yes | GEMM (prefill) / GEMV (decode)
RoPE | Yes | Disabled | Strided DSD @fmulh bug in decode
KV Cache Write | No (allocated) | Yes | Incremental write in decode
Causal Masking | No | N/A | Autoregressive by nature in decode
Score: Q @ K^T | Yes | Yes | Variable-length in decode
Softmax | Yes | Yes | fast_exp() approx in decode
Output: attn @ V | Yes | Yes | 4 variants in decode
O-Projection | Yes | Yes | 
Residual Add | Yes | Yes | 
RMSNorm (pre-FFN) | Yes | Yes | 
UP Projection (SwiGLU) | Yes | Yes | 
GATE Projection (SwiGLU) | Yes | Yes | 
SiLU Activation | Yes | Yes | 
DOWN Projection | Yes | Yes | 
FFN Residual Add | Yes | Yes | 

## Slide 3
Missing Operators & Features for Llama3-8B
End-to-end inference requires these additional components beyond the single-layer implementation
Priority | Operator / Feature | Complexity | Notes
P0 | Fix RoPE in Decode | Medium | Debug strided DSD bug or restructure memory layout
P0 | Causal Mask in Prefill | Low | Add -inf masking to upper triangle before softmax
P0 | Multi-Layer Loop + Weight Mgmt | High | 32 layers; weight streaming or full on-chip storage
P0 | LM Head (Vocab Projection) | High | 4096 -> 128,256 GEMV; largest single operation (~1 GB)
P0 | Sampling (argmax minimum) | Medium | Distributed argmax reduction over 128K sharded logits
P1 | Token Embedding Lookup | Medium | Host-side compute + transfer, or on-chip scatter
P1 | Final RMSNorm | Low | Reuse existing RMSNorm kernel with separate weight vector
P1 | Per-Layer KV Cache Management | High | 32 x KV caches; memory allocation strategy needed
P1 | Host <-> WSE Orchestration | High | Weight loading, token I/O loop, pipeline control
P2 | Top-k / Top-p Sampling | Medium | More complex distributed reduction
P2 | Tokenizer / Detokenizer | Low | Host-side; use existing libraries (tiktoken)

## Slide 4
Llama3-8B Inference Pipeline
Green = implemented | Red = missing | Yellow = partially implemented / broken
Tokenizer (Host CPU)
BPE tokenization 128K vocab
Embedding Lookup
128256 x 4096 ~1 GB table
Transformer x 32 Layers
Single layer done Need loop + weights
Final RMSNorm
Reuse kernel New weights
LM Head (Vocab Proj)
4096 -> 128256 Largest GEMV
Sampling (argmax/top-k)
Distributed reduction
Detokenizer (Host CPU)
Token -> text
Inside Each Transformer Layer (implemented):
RMSNorm -> Q/K/V Proj -> RoPE* -> Score (Q@K^T) -> Causal Mask** -> Softmax -> Attn@V -> O-Proj -> Residual Add
RMSNorm -> UP Proj -> GATE Proj -> SiLU -> DOWN Proj -> Residual Add
* RoPE disabled in Decode (strided DSD bug) ** Causal mask missing in Prefill

## Slide 5
P0 Critical Items - Detail
Fix RoPE in Decode [Medium]
RoPE is disabled due to a strided DSD @fmulh bug. Without positional encoding, the model produces garbage. Options: (a) fix the strided DSD issue, (b) restructure memory layout to avoid strided access, (c) pre-apply RoPE on host.
Causal Mask in Prefill [Low]
Current prefill computes full seq_len x seq_len attention with no mask. Need to set upper-triangle scores to -inf before softmax. Simple element-wise operation on the score matrix.
Multi-Layer Loop + Weight Management [High]
Llama3-8B has 32 layers. Options: (a) weight streaming from host per layer (~14 GB total), (b) all weights on-chip (feasible on WSE-3 ~40 GB SRAM), (c) hybrid. Each layer needs separate weights and KV cache.
LM Head (Vocab Projection) [High]
Final [1, 4096] x [4096, 128256] projection. The weight matrix alone is ~1 GB in f16. Llama3 ties embedding and LM head weights. Requires new sharding strategy for the extremely wide output dimension.
Sampling (argmax) [Medium]
Distributed argmax over 128K logits sharded across PEs. Need a new reduction primitive that returns both max value and its index. Temperature scaling is a simple element-wise multiply before argmax.

## Slide 6
P1 / P2 Items
[P1] Token Embedding Lookup [Medium]
Convert token IDs to 4096-dim vectors. 128256 x 4096 table (~1 GB). Can be done on host and transferred, or implement on-chip indexed scatter.
[P1] Final RMSNorm [Low]
Same kernel as existing RMSNorm, just needs to be invoked post-loop with a separate weight vector. Minimal new code.
[P1] Per-Layer KV Cache Management [High]
32 layers x KV cache. At seq_len=8192: ~512 MB total. Need memory allocation strategy across PEs and lifetime management.
[P1] Host <-> WSE Orchestration [High]
Full pipeline control: weight loading, token I/O per decode step, KV cache init from prefill. Extend launch scripts to loop.
[P2] Top-k / Top-p Sampling [Medium]
More sophisticated sampling beyond argmax. Requires distributed partial sort or threshold-based filtering across PEs.
[P2] Tokenizer / Detokenizer [Low]
Host-side only. Use tiktoken or sentencepiece. Not a WSE operator.

## Slide 7
Llama3-8B Memory Budget on WSE-3
Component | Size (f16) | Per Layer | Total (32 layers)
Q / K / V / O Weights | 4 x 4096 x 4096 x 2B = 128 MB* | 128 MB | ~4 GB
(GQA: K,V are 4096x1024) | Q,O: 64 MB + K,V: 16 MB = 96 MB | 96 MB | ~3 GB
FFN Weights (UP+GATE+DOWN) | 3 x 4096 x 14336 x 2B = 336 MB | 336 MB | ~10.5 GB
RMSNorm Weights | 2 x 4096 x 2B = 16 KB | 16 KB | ~0.5 MB
KV Cache (seq=8192, bsz=1) | 2 x 8 x 128 x 8192 x 2B = 32 MB | 32 MB | ~1 GB
Embedding / LM Head | 128256 x 4096 x 2B = 1 GB | -- | 1 GB (shared)
Total |  |  | ~15.5 GB
WSE-3 has ~40 GB distributed SRAM across all PEs. Llama3-8B at ~15.5 GB fits comfortably with room for activations and intermediates. All-on-chip strategy is feasible -- no weight streaming required.